## Slide 1
Technology
ICT
Option: Data Representation
Notes: <number>

## Slide 2: Data Representation
In our everyday lives, we communicate with each other using analogue data.
This data takes the form of:
  Sound
  Images
  Letters
  Numbers
  Colours etc.
This type of data can vary and because of this, it cannot be easily represented in a computer.
Notes: <number>

## Slide 3: Data Representation
Computer - electronic device - handles binary data
Transistors represent the binary data.
  Transistor is on - binary 1
  Transistor off - binary 0.
Using transistors, binary codes are devised to represent numbers, letters, colours, sounds etc.
In this binary system, each 0 or 1 is called a binary digit (Bit). By placing them side by side, we can create binary codes
0 | 1 Bit
10 | 2 Bit
1011 | 4 Bit
10010011 | 8 Bit
Notes: <number>

## Slide 4: Data Representation
If we extend this system, we could use it to represent numbers. From the right-hand side, the binary digits could represent the numbers 128, 64, 32, 16, 8, 4, 2, 1 etc.
Decimal Number
Binary
Decimal Number
Binary
0
0
12
1100
1
1
16
10000
2
10
32
100000
3
11
60
111100
4
100
100
1100100
5
101
111
1101111
6
110
156
10011100
7
111
185
10111001
8
1000
223
11011111
Decimal Number
Binary
Decimal Number
Binary
0
0
12
1100
1
1
16
10000
2
10
32
100000
3
11
60
111100
4
100
100
1100100
5
101
111
1101111
6
110
156
10011100
7
111
185
10111001
8
1000
223
11011111
Decimal Number
Binary
Decimal Number
Binary
0
0
12
1100
1
1
16
10000
2
10
32
100000
3
11
60
111100
4
100
100
1100100
5
101
111
1101111
6
110
156
10011100
7
111
185
10111001
8
1000
223
11011111
Decimal Number
Binary
Decimal Number
Binary
0
0
12
1100
1
1
16
10000
2
10
32
100000
3
11
60
111100
4
100
100
1100100
5
101
111
1101111
6
110
156
10011100
7
111
185
10111001
8
1000
223
11011111
Notes: <number>

## Slide 5: Data Representation
From the numbers example, we can see that the computer can handle data as long as it is presented in binary form.
The analogue numbers have become digital data. If it was possible to create codes to represent all our analogue data, it would appear as groups of 0’s and 1’s and could be converted to digital data. The computer could then handle this data.
This conversion process is called digitising data:
RED
Is there anybody there, said the
traveller,
knocking on the
101101001001000010010001000100001011010101010101111000101010101010001010011111001010100101010101010101010011100110010101111010100101010001010101001010010100101000100011
Notes: <number>

## Slide 6: Data Representation
Word-procressing is the most basic type of data processing. In Wordprocessing, the keyboard holds the character set which includes:
  The alphabet in upper and lower case
  The numbers from 0 to 9
  Misc. characters - space, &, %, £, €, ½, ? Etc.
To digitise these characters, a sequence of 8-Bits (0’s and 1’s) is allocated to each character. This sequence of 8-Bits is called a Byte.
A Byte is the amount of storage required to store one character from the character set.
Notes: <number>

## Slide 7: Data Representation
It is possible to represent 256 characters using this system.
A Byte sequence is assigned to each character on the keyboard and there are lots to spare for special characters etc.
These Byte codes can be set in a table to produce the American Standard Code for Information Interchange (ASCII).
If a character from the table is typed into the computer, it will occupy 1 Byte of the computers main memory (RAM) and if it is saved to a disk drive, it will occupy 1 Byte of storage space.
Therefore:
  T4 is 2 Bytes long
  Technology is 10 Bytes long
  Design and Communications Graphics is 34 Bytes long (the 3 spaces count)
Notes: <number>

## Slide 8: Data Representation
In the ASCII table, the bit sequences (codes) are listed in Binary and each code is named according to its Decimal value:
The 256 codes are divided into sections:
  0 to 31 - System codes - Esc (27), Backspace (8)
  32 to 127 - Lower ACSII - common keyboard characters.
  128 to 254 - Higher ASCII - Newer codes like the € and language symbols
Notes: <number>

## Slide 9: Data Representation
When the computer keyboard is being used, the ASCII codes are sent to the computer as the characters are typed:
0101010000110100
The computer combines the stream of Bits into Bytes:
01010100 and 00110100
These are then converted to ASCII numbers (84 and 52) and displayed on screen:
T4
Notes: <number>

## Slide 10: Data Representation
Not all data can be represented as characters
To process images and sound in a computer, they must be represented as binary codes.
An image can be represented as a map of binary codes
If the image is zoomed, the individual pixels can be seen as either black or white.
In a black and white image, only 1 Bit is needed to represent each pixel as the pixel can only be black or white.
Notes: <number>

## Slide 11: Data Representation
This is called a Bitmapped image as the bits used to represent the image are arranged into a grid of Bits
A more complex image is shown below and the grid and map of Bits is clearly visible:
The only difference between this and a colour image is the number of Bits needed to represent each pixel
In 24-bit colour, 24 Bits are needed for each pixel etc
Notes: <number>

## Slide 12: Data Representation
Sound can also be stored in a computer as binary codes
Analogue sound is represented as a wave.
To represent the varying values of a soundwave, it’s height must be measured at regular intervals and the measurements given binary codes.
This process is called Sampling and the number of samples taken in a second is called the sampling rate
The sampled measurements make up the digital sound file
Sampling rate
Analogue signal
Time
Amplitude
Notes: <number>