## Slide 1
Technology
ICT
Option: Networks
Notes: <number>

## Slide 2: Networks
Networking - sharing information and resources
Computers connected to a network can:
  Share a printer or a plotter among several users
  Share files with other users
  Share an Internet connection
  Share a folder for central storage of student assignments etc.
The two main network types are:
  Peer networks - organised as Workgroups. Members simply share their resources with their peers. They are:
  Relatively inexpensive to set up
  Easy to set up
  No special software is required
  No central storage is provided
  They have poor security
Notes: <number>

## Slide 3: Networks
  Client server networks - in these networks, Dedicated Servers control Log In and access to resources
  User Level access applies here
  Every user has a User Account and must supply a Username and Password to get access to the network
  Permissions are applied to user accounts and these control access to resources
Their main features are:
  They have excellent security
  Central storage of assignments
  Expensive dedicated hardware (server) is required
  Expensive dedicated networking software and user licenses required.
  A fee called a client access license (CAL) must be paid for each client connecting to the server.
  A network administrator is required
Notes: <number>

## Slide 4: Networks
Local area networks (LAN)
  Computers connected together in a single location
  Vary in size from two computers connected together to share a printer or Internet connection, to several computers connected over multiple floors of a building
  Computers connected using some form of cable (or wireless) and all the components of the LAN will be owned locally
  Network devices are called Nodes. (computer, printer etc.)
Notes: <number>

## Slide 5: Networks
Wide area networks (WAN)
  In a wide area network, the network extends beyond the confines of a single building or buildings and some form of telecommunications must be used to connect the computers
  All the network components will not be owned locally
  The Internet is the largest WAN in existence
Notes: <number>

## Slide 6: Networks
Topology refers to the physical layout of the network - how the network is cabled.
The Ethernet standard is used in most networks:
  Star topology - In a star topology, each computer is cabled to a central switch. A switch is like a junction box and when a computer sends a signal, the switch sends it to the relevant computer(s) on the network
Notes: <number>

## Slide 7: Networks
Specifications
  Maximum cable (segment) length is 100 metres from a computer to a switch
Advantages of the Star topology:
  Easy to troubleshoot as LED’s on the front panel of the switch show the status of each computer connected to it
  Expansion is easy as you just cable a new computer to the switch. If all the ports on the switch are used, a higher capacity one can be used or a second switch can be stacked on top of the first one and linked to it
  Damaged or loose cables only isolate the specific computers and the network continues working
Obviously, switch failure will stop the network from working
Notes: <number>

## Slide 8: Networks
Network Media
Network media can be divided into 2 categories:
  Network interface cards (NIC’s)
  Cables
1. Network interface cards:
Network cards usually fit into slots on the Mainboard of the computer. They are categorised by:
  Type (PCI, USB or PC-Card)
PCI
Wireless PCI
PC-Card
USB
Notes: <number>

## Slide 9: Networks
  The type of cable they support
  Their data transfer rate
    Fast Ethernet - 100Mbps using UTP
    Gigabyte Ethernet - 1000Mbps using UTP
Notes: <number>

## Slide 10: Networks
Network cables
Several factors affect the choice of cable for a particular network installation:
  The distance between computers
  The physical environment in which the cables must operate (electrical interference)
  The type of network being installed
Copper and aluminium are used in network cables because they are good conductors
This is also their downfall as they can conduct signals (RF noise) from electric wiring etc. and this interferes with the data being transmitted on the network
Because of this, methods of shielding the copper and aluminium wire have been developed
Notes: <number>

## Slide 11: Networks
Twisted pair cable - works on the principle that two conductors wrapped or twisted around each other generate a field that protects them from RF noise. The degree of twisting on each pair is varied along it’s length to reduce crosstalk between the pairs. There are two main types:
  Shielded Twisted Pair (STP)
  Unshielded Twisted Pair (UTP)
Shielded twisted pair - each twisted pair is insulated using metal foil to reduce crosstalk. The shielded pairs are encased in a second shielding layer to reduce RF noise and finally, an outer plastic jacket is added to protect the cable from damage. This is expensive cable and it is difficult to install. It is only used where UTP is unsuitable
Twisted pairs
Plastic jacket
Notes: <number>

## Slide 12: Networks
Unshielded twisted pair (UTP) - is nowadays the most common network cable in use. Category 6 UTP is the modern standard. It uses four pairs of twisted wires covered with a plastic jacket. It is susceptible to RF noise which limits it’s data transmission speed and maximum cable length. and so shouldn’t be laid over fluorescent lights or in conduits along with electric wires. It’s main features are:
  The cheapest cable
  The maximum length of a single cable is 100 meters
  Maximum data transmission rate is 1000Mbps
  Susceptible to RF noise
  Switches are required
Twisted pairs
Plastic jacket
Notes: <number>

## Slide 13: Networks
Fibre optic cable - transmit s data as light pulses instead of electrical pulses. As a result, they are immune to crosstalk and RF noise. Because of this, signals travel further
Features:
  Immune to crosstalk and RF noise
  Provides secure data transmission
  Very expensive (up to ten times more expensive than UTP)
  Difficult to install as cable can easily be damaged by bending
  Single cable can extend for several kilometres
Fibre core
Jacket
Kevlar Shield
Insulation
Notes: <number>

## Slide 14: Networks
Wireless networks - allow you to connect your computers without the need for cables
They offer the same flexibility as mobile phones, but are currently restricted to approximately 50 metres radius from the transmission switch (Access Point)
They can be used to link PC’s, Laptops or a combination of both
They can be linked to form a full wireless LAN or linked to an existing Ethernet LAN (hybrid network)
Technically, there are two types of wireless transmission:
  Infrared (IR) - devices must have line of sight between them as infrared signals can’t penetrate solid objects, including people. For this reason, infrared tends to be used for wireless mice, keyboards etc
  Radio frequency (RF) - Radio frequency devices don’t need line of sight as radio waves can penetrate solid objects. This makes them much more suitable for LAN’s
Notes: <number>

## Slide 15: Networks
Wireless standards
IEEE 802.11 is the standard used for wireless LAN’s
This originally had a transmission speed of 2Mbps
More recently, a range of new standards have appeared
When buying wireless LAN devices, make sure that they follow the IEEE 802.11 standards as this will offer most flexibility and there is a much wider choice available
Use single protocol devices if possible
Notes: <number>

## Slide 16: Networks
Wireless LAN operation
At their most basic, a wireless LAN can be two computers fitted with wireless network interface cards for communication with each other when they are in range
This is called an Ad Hoc wireless LAN and is the equivalent of an Ethernet Peer to Peer LAN
Other computers can join the LAN as they come into range
The network interface card set up is similar to that for standard Ethernet and each card comes with it’s own network set up software
Notes: <number>

## Slide 17: Networks
A more common use of wireless LAN would be to connect it to an existing Ethernet Server or an Ethernet LAN to produce an Infrastructural LAN
A device called an Access Point (Ethernet Bridge or Base Station) connects to the Ethernet LAN and provides access for the wireless computers
It is possible to connect in excess of 30 computers to an access point Access points can be connected to each other to extend the network
Notes: <number>

## Slide 18: Networks
Finally, a Directional Antenna can be used to link wireless LAN’s over large distances ( up to several kilometres)
This could be used to link schools together or to link campus buildings
The connection software to enable communication between the client computer and the access point is loaded on the client computer as well as the software driver for the network card
Notes: <number>

## Slide 19: Networks
LAN EXPANSION
Electrical signals weaken over distance
This is called Attenuation and it limits the length of cable a signal can travel through before it becomes unusable
Interference from electrical installations etc. also effect the distance
If you want a signal to travel over a longer distance, the signal must be repeated and retransmitted.
LAN expansion will either involve adding more computers etc. to your existing network or combining smaller LAN’s (Segments) to form larger ones
Many devices are available:
  Hub
  Switch
  Router
Notes: <number>

## Slide 20: Networks
Hub
At their simplest, hubs are basically multiport repeaters
Each computer on the network connects to the hub
When a computer on the network transmits data, it travels along the UTP cable to the hub
The hub simply broadcasts the signal to all the computers on the network
Hubs are available in a number of capacities ranging from 4-port to 24-port They can also be stacked to increase capacity
LED’s on the front of the hub indicate the status of each port
They should not be used in a modern network
Hub
Notes: <number>

## Slide 21: Networks
Switch
A switch is basically a clever hub
They are available with varying port numbers and can be stacked
A switch keeps a table of the destination address of each computer connected to it
It doesn’t broadcast data to all computers like a hub would, it instead only sends the data to the computer whose destination address is in the data Switches greatly reduce the amount of network traffic
Switch
Notes: <number>

## Slide 22: Networks
Router
Routers are used to connect multiple networks (Internet)
They choose the best path for the data through the networks
Routers keep tables (routing tables) of other routers on the Internet
When a router receives data, it consults it’s table and works out the best route for the data to it’s destination
Notes: <number>

## Slide 23: Networks
Network Protocol
A Network Protocol is a set of rules defining the method of communication between the computers on the network or between networks
The protocol controls how data is split up, addressed and how it is transmitted over the network(s)
The Ethernet standard is usually used with Microsoft Networking and TCP/IP is the protocol used:
  TCP/IP - this protocol suite is the most common suite in use today. The Internet uses TCP/IP so it must be installed to use the Internet. It also allows different computer types to communicate - so, PC’s, UNIX, LINUX and Mac’s can all communicate with each other
Notes: <number>

## Slide 24: Networks
Configuring TCP/IP
To get TCP/IP to work properly, you need to set an IP Address and a Subnet Mask. The addresses are written in a notation called Dotted Quad - (xxx.xxx.xxx.xxx)
Notes: <number>

## Slide 25: Networks
  IP Address - identifies the computer on the network. Each computer on the network must have a unique IP address. 192.168.0.1,192.168.0.2, 192.168.0.3, 192.168.1.4 etc
  Subnet Mask - identifies the network your computer is on. Computer son the network must have the same subnet mask - 255.255.255.0
  Default Gateway - the IP address of the Router. This address will be used for Internet access through the network. When a computer requires Interned access, it will use this address to contact the router and the router will supply the connection to the Internet
  DNS - every web site is known to computers by it’s IP address but we know them by there Domain Name System name. DNS is a database used to link the domain name (www.t4.ie) to it’s actual IP Address (32.195.130.32). It is basically the Internet’s phonebook
Notes: <number>