## Slide 1
Structures
and
Mechanisms

## Slide 2: Cam and Follower
Cam
Follower
The cam and follower is a device which can convert rotary motion (circular motion) into linear motion (movement in a straight line).
Followers (valves)
Cams

## Slide 3: Cam and Follower
The cam can have various shapes. These are know as cam profiles.
Pear
Heart
Circular
Drop
Cam
follower

## Slide 4: Cam and Follower
A follower is a component which is designed to move up and down as it follows the edge of the cam.
Knife edge
Follower
Flat foot
follower
Off set
follower
Roller
follower
cam
Follower

## Slide 5: Cam and Follower
The 'bumps' on a cam are called lobes.
The square cam illustrated has four lobes, and lifts the follower four times each revolution.
Square cam
Follower
Examples of other rotary cam profiles.

## Slide 6: Cam and Follower
Examples of a Rotary cams in operation.
Control the movement of the engine valves.
Cams used in a pump.

## Slide 7: Cam and Follower
The linear cam moves backwards and forwards in a reciprocating motion.
Linear cam
Distance moved by the follower
Cam Follower

## Slide 8: Cam and Follower
Cams can also be cylindrical in shape
Below a cylindrical cam and roller follower.
The cam follower does not have to move up and down - it can be an oscillating lever as shown above.
Cam rise and Fall
Max Lift
Min Lift