## Slide 1
Structures
and
Mechanisms

## Slide 2: Gears
A gear is a wheel with teeth on its outer edge.
The teeth of one gear mesh (or engage) with the teeth of another.
Above
Gears meshing or engaged

## Slide 3: Gears
Driver and Driven
Two meshed gears always rotate in opposite directions.
Driver gear
Driven gear
Spur Gears

## Slide 4: Gears
Idler gear
Driver
Driven
Idler gear

## Slide 5: Gears
Multiple gears can be connected together to form a gear train.
Simple Gear Train
Each shaft carries only one gear wheel.
Intermediate gears are known as Idler Gears.

## Slide 6: Gears
Compound Gear Train
Driver
Compound Gear
Driven
If two gear wheels are mounted on a common shaft then it’s a Compound Gear train.

## Slide 7: Gears
Generally, the Gear Ratio is calculated by counting the teeth of the two gears, and applying the following formula:
Gear ratio = Number of teeth on driven gear
Number of teeth on driver gear
Gear Ratio

## Slide 8: Gears
Gear Ratio - Calculation
A 100 tooth gear drives a 25 tooth gear. Calculate the gear ratio for the meshing teeth.
Gear ratio = Number of teeth on driven gear
Number of teeth on driver gear
Gear ratio = driven 25 = 1
driver 100 4
This is written as 1:4

## Slide 9: Gears
Gear Speed :- Calculation
A motor gear has 28 teeth and revolves at 100 rev/min. The driven gear has 10 teeth. What is its rotational speed?
Speed of driven gear = Number of teeth on driver gear x 100
Number of teeth on driven gear
Speed of driven gear = driver = 28 x 100 = 280 rev/min
driven 10
28 teeth, driver
10 teeth, driven

## Slide 10: Gears
The worm gear is always the drive gear
Worm and wheel
Worm gear and wheel

## Slide 11: Gears
The rack and pinion gear is used to convert between rotary and linear motion.
Rack and Pinion
Heavy Duty
Car Jack

## Slide 12: Gears
Bevel gears are used to transfer drive through an angle of 90o.
Bevel Gears
Bevel gears

## Slide 13: Important Calculations : -
Work Done = Force x Distance moved in the direction of the force
Power =
Total Time Taken
Total Work Done
Efficiency % =
Power Output
Power Input
Friction: - Resists the movement of one surface over another
X 100
Efficiency = Mechanical advantage
Velocity ratio