## Slide 1
Mechanisms

## Slide 2: Moments
In order to understand Mechanisms better, we need to understand pivots, moments and equilibrium.
Boom
Counter balance weight

## Slide 3: Equilibrium
When something is balanced it is said to be in equilibrium.
Pivot point
Or
fulcrum
Fulcrum

## Slide 4: Moments
The Moment of a Force is the force multiplied by the distance from the pivot point.
Moment = F x d
Distance (d)
Force (F)
Fulcrum

## Slide 5: Moments
Torque may be represented as shown.
Torque (turning force) = Force x Distance
Pivot Point
Force

## Slide 6: The Principle of Moments
The Principle of Moments states, that for there to be equilibrium, the clockwise moments must equal the anti-clockwise moments.
Clockwise Moments = F2 x d2
Anti-clockwise Moments = F1 x d1
If F2 x d2 = F1 x d1 there is equilibrium
Balanced when f1xd1 = f2xd2

## Slide 7: The Principle of Moments
Clockwise Moments = F2 x d2 = 20nx1m = 20Nm
Anti-clockwise Moments = F1 x d1 = 10Nx2m = 20Nm
If F2 x d2 = F1 x d1 there is equilibrium
20Nm = 20Nm, Therefore, the loaded beam is in equilibrium.
f2
f1
d1
d2

## Slide 8: Levers
Definition
A lever is a rigid rod,
pivoted about a fixed
point or axis,
which is known as the
fulcrum.
lever
Effort
Fulcrum
Load
fulcrum

## Slide 9: Levers
There are three types or class of lever.
Class three
Class two
Class one
Examples: Seesaw
Crow bar
Scissors
Examples: Wheelbarrow
Micro switch
Brake pedal
Example: Shovel
Fishing rod
Forearm muscles

## Slide 10: Levers
Class One Levers
See-saw
Crowbar

## Slide 11: Levers
Class Two Levers
Wheel Barrow
Brake pedal

## Slide 12: Levers
Class Three Levers
Fishing rod
Shovel

## Slide 13: Mechanical Advantage
Mechanical Advantage = Load
Effort
Man lifting a Stone with a Lever
Load
Effort
Fulcrum
Lever

## Slide 14: Mechanical Advantage
Mechanical Advantage - Calculation
To raise a weight 400N.
It was found that the weight could be lifted with an effort of 100N.
What is the Mechanical Advantage of the mechanism?
Mechanical Advantage = Load = 400N = 4:1 or 4
Effort 100N
Load
Effort

## Slide 15: Velocity Ratio
Load
Lever
The Velocity Ratio = Distance moved by effort
Distance moved by load
Distance moved
by effort
Distance moved
By load

## Slide 16: Velocity Ratio
Velocity Ratio - Calculation
The 500N weight is moved with an effort of 100N.
The distance moved is shown
What is the Velocity Ratio of the mechanism?
Distance moved
by effort
85cm
Velocity Ratio = distance moved by effort = 85cm
distance moved by load = 17cm = 5:1 or 5
Distance moved
by load
17cm