## Slide 1
Structures
and
Mechanisms

## Slide 2: Pulleys
A pulley wheel is a mechanism which helps move or lift objects.
pulley
Exercise machine

## Slide 3: Pulleys
Parts of a Pulley System
Direction of Force
Notice that the pulleys change the direction of the applied force.

## Slide 4: Pulleys
Types of Pulley.
A ski lift operates on a fixed pulley system
1. A fixed pulley

## Slide 5: Pulleys
2. A moveable pulley - rises and falls with the load being moved.
Moveable pulley

## Slide 6: Pulleys
Block and tackle
3. A block and tackle - Consists of two or more pulleys (fixed and moveable).

## Slide 7: Pulleys
In this simple pulley system,
the force is equal to the load,
so the Mechanical Advantage is 1:1 or 1.
The Pulley Advantage
10 Kg = 100 N
The Mechanical Advantage is calculated like so:
Mechanical Advantage = Load / Effort = 100 N / 100 N
Mechanical Advantage = 1:1 or 1

## Slide 8: Pulleys
Each side of the rope carries half the load.
Therefore, the force required by the person to
keep the load in equilibrium is also half the load.
This system has a
Mechanical Advantage of 2:1 or 2.
The Pulley Advantage
The Mechanical Advantage is calculated like so:
Mechanical Advantage = Load / Effort = 100 N / 50 N
Mechanical Advantage = 2:1 or 2
10 Kg = 100 N

## Slide 9: Pulleys
This system has a
Mechanical Advantage of 4:1 or 4.
The Pulley Advantage
10 Kg = 100 N
The Mechanical Advantage is calculated like so:
Mechanical Advantage = Load / Effort = 100 N / 25 N
Mechanical Advantage = 4:1 or 4

## Slide 10: Pulleys
This system has a
Mechanical Advantage of 4:1 or 4.
The Pulley Advantage
The Mechanical Advantage is calculated like so:
Mechanical Advantage = Load / Effort = 2000 N / 500 N
Mechanical Advantage = 4:1 or 4
200 Kg = 2000 N

## Slide 11: Pulleys
Using pulleys to transmit motion and force:
Pulleys and Belts
Toothed Belt and Pulleys
?
Pulley drives:

## Slide 12: Pulleys
Pulley drive calculations:
Driver 40 mm Dia.
280 rev/min
Driven 70 mm Dia.
? rev/min
Driven will rotate slower than the driver.
Calculation: -
Speed ratio =
Diameter of Driver pulley
Diameter of Driven pulley
=
40
70
Speed of Driven pulley =
280 x
40
70
= 160 rev/min
How could you change the direction of rotation of the driven pulley ?