## Slide 1
Design and Manufacturing
Projects 1 & 2 - Desk Fan
Notes: <number>

## Slide 2
Design for Manufacturing
Design Brief: Design and Manufacture a Working Model Electric Fan
Project Option 1
Project Option 2
These are Integrated projects covering a range of processes and manufacturing skills including Design, Mechanisms, Electronics control, CNC machining, Vacuum Forming etc.

## Slide 3
The design must be manufactured using the
materials supplied and incorporate the following:
Have a vacuum formed base that will support the fan and house the Electronic circuit, Switch & 3 Volt battery
Have a 8Ø brass support bracket that will locate the motor,
and the support base in appropriate position.
The fan must have a variable Electronic Speed control circuit.
All electrical connections must be soldered.
Each student should endeavor to individualize her/his design.
Design for Manufacturing. - Project Option 1
The rational behind this Project is that it will allow the teacher to Manage the Design & Manufacturing Process within the constraints of the Classroom/Workshop environment. E.g., Materials, Cost, Machines & Equipment, Time, Reduced Waste & Health & Safety.

## Slide 4
Given an MDF block 125 x 75 x 20 mm design a basic shape to encapsulate the components, support the mechanisms and house the electronic controls.
Mould Manufacture – 1 Design Variations
Examples of six Pattern Designs from the MDF blank
Refinement to the mould may be by achieved using readily available components in the workshop e.g. coins, washers, rivets, expanded polystyrene shapes, badges etc.

## Slide 5
Mould Manufacture - 2
Without proper draft the mould cannot be removed from the vacuum formed case without damaging it.
Tilting the table on a Scroll saw or Band
saw will give the necessary angle but will require finishing by a sanding block.
Wood Plane used to get Draft
Table set to 5º on Belt Sander
A most important requirement in mould design is DRAFT which must be al least 3 to 5 º.
Wood chisel used to get Draft

## Slide 6
Mould Manufacture - 3
Internal holes or cavities in a mould must have 2Ø mm drilled holes through to the base of the mould so as all air can be removed by the vacuum pump.
The base of the mould may be drilled and treaded M6 to allow a handle to be attached to assist in pull the mould from the formed shape.
A mould may be dusted with talcum powder to assist in releasing them from the formed shape.
VACUUM FORMING MACHINE
Turn on the Vacuum Forming at least 30min before use.
Set outside Temperature Zones set to full power
Set centre Temperature Zones set to 75% power.
Do not over heat the Polyester sheet asit will sag.

## Slide 7
Finished base made from 2 mm Polystyrenes is trimmed to shape using:
A band-saw.
Tin snips.
GERBIL cutter.
(A Gerbil is a multi-purpose Vacuum Forming cutting & Finishing Machine).
A Tungsten Carbide cutting tool is used for creating a 10 mm flange around the edge of vacuum forms. This add considerable strength to the Form.
A belt sander, a file or a sanding block may also be used to finish Forms.
Finishing a Vacuum Formed Object
The finished fan base is then drilled to accommodate Switches, Variable resistor, LED and pulley mechanism support etc.

## Slide 8
Desk Fan 2
Parts and Dimensioned drawings for Desk Fan 2
Vacuum Formed Base
Supplied Parts
Speed control circuit & Motor
Base Dimensions
Fan Stand & Alternative Design
Brass washer

## Slide 9
Making the Brass support Bar
Facing in the Lathe
Centre Drilling in the Lathe
Accurate Tapping in the Lathe
Advanced design options may include:
Allow the fan direction to be adjustable.
A mechanism that will make the fan oscillate

## Slide 10
Completed Variable speed Model Fan
A PCB mounted electronic circuit using a TIP 121 chip is used to provide a range of speeds.
Note that motor holder has been spray painted.
Model Fan has been drawn up and fully rendered in Solid Works.
Assembled Project 2

## Slide 11
Completed Project 1.
Assembled fixed speed Model Fan assembled using parts provided.
Model Fan has been drawn up and
fully rendered in Solid Works.
A larger diameter Propeller and Solar Motor will change this project to a Generator. Add two LED to indicate current Output

## Slide 12
Manufacture of the bracket Project 1
Bracket is marked out, shaped, drilled, then polished before bending.
The Bracket must be accurately bent using a Bending Machine or Folding Bars
Dimensions for Vacuum Form for Base.

## Slide 13
Bracket Design - Project 2
Given a Brass strip 30 x 165 x 1 mm design alternative of support brackets that will;
Support the drive shaft.
Hold the motor in position.
Provide for the bracket to be attached to the base.

## Slide 14
Advanced option 3 for this Project.
Gear or chain drive may be used.
A mechanism designed to allow the fan to oscillate.
Reversible DPDT Centre “Off” Switch is fitted.
Red/Green LED fitted to indicate Forward/Reverse.
The speed control may be recycled for use in any motorized project
Design and make a brass fan rotor.
The cone may be made on the made on a CNC lathe.
The fan is soldered to a brass cone.
Brass Cone is Screwed & Tapped M5.
Brass Cone soldered to Rotor

## Slide 15
Summary
Most or all of the following headings with associated theory may be integrated into the overall design project.
Design theory and practice
Appropriate material selection
Marking out and fitting skills
Assembly and joining processes
Electronic circuit design theory and practice
PCB Wizard & Solid Works
Mould making theory and practice
Finishes, polishing, spray painting of surface.
Project Management
Workshop Safety considerations
Remember “Design is not always about Inspiration and Genius”
It is mostly about “Perspiration and Hard Work”
Notes: <number>