## Slide 1
Design and make a vehicle that will travel exactly 1 Metre and
then stop

## Slide 2
Motion / Vehicle
Simple design - one piece frame or body to support additional components
- design to incorporate an existing circuit from phase 2
- Monostable 555 timer circuit chosen
- Circuit may be a separate board or Milled/cut from a copper clad board which could also be the support frame
- Electronic components mounted directly to the frame/body
Prototype vehicle:

## Slide 3
Motion / Vehicle
Prototype vehicle:
An additional transistor required in the circuit to drive the relay as the output on pin 3 not sufficient to drive the relay directly.
Separate power supply used to drive the motor.
Polycarbonate body frame shaped and drilled with motor mounted directly to frame.
Worm gear system to drive the rear wheels.
Separate circuit board, attached to the frame.
A monostable 555 timer circuit used.
Travel distance obtained by adjusting the Resistance/ Capacitance values in the potential divider circuit.
The output on pin 3 timed to give required travel depending on the gearing system used.

## Slide 4
Motion / Vehicle
Additional views of components and assemblies mounted to the frame
Circuit with additional components added.
Notes: Student: An knowledge of construction and manufacturing techniques and processes will be of benefit
when considering appropriate ideas / concepts when designing for manufacture.
Teachers should model (designing) demonstrate how we think, see shapes and form, use reference materials and mood boards to generate ideas. Also, show how an idea/concept can be developed in design detail and showing constructional details i.e. how the parts intend to fit together. Showing how the pcb, battery are located and secured?

## Slide 5
Motion / vehicle
Integration of Topics:
Body/Frame design:
Sketching of idea’s, dimensioning, selection of suitable materials
Processes used:
Marking out, cutting, filing, drilling, bending, etc.
Assembly Techniques:
Screwing and Tapping, Soldering, Pop riveting, Adhesives.
Drive Systems:
Gear boxes ,Both bought and constructed, Bevel gears, Worm Gears, Pulley Systems, Belt & Chain Drives, Drive reversal, etc.
Finishes:
Polishing, Painting, Vacuum forming of exterior shell.
Electronics:
Components, Circuit design, Board layout, Timing circuits, Electronic theory.
Most or all of the above with associated theory may be integrated into the overall design project
Project Management
Allocation of resources, Time, Materials, Equipment, Costs, etc
Notes: Designing for manufacturing – students should show graphically how the parts fit together; use notes / annotation
to help explain your ideas / thinking!

## Slide 6
Motion / Vehicle
Project management – applied to project
Differentiation by task parameters – 3 scenarios
  simple construction
  polycarbonate model
  vacuum formed body feature
Elements of control
Power and energy – motor operation
Notes: The dimensions of the wooden blocks will be calculated by the teacher and this is the starting point for the student.
Knowledge of the vacuum forming process is important before starting to design.
Where possible use 2-3mm rigid polystyrene sheet to accommodate complex shapes which also provides rigidity and a feeling of quality.

## Slide 7
Motion / Vehicle
Mould design:
Original moulds may be made by gluing layers of material together and then shaping using a variety of tools and methods to arrive at the required shape.
Materials may be MDF, Balsa wood, Modelling clay, etc,
When using wood as a mould material the bottom layer is usually glued separated by a sheet of paper so that it may be easily removed and used as the base for your vehicle
Vacuum forming then used to obtain the finished product.
Rough sample shown in the next slide
Mould design important when considering the easy removal of the vacuum formed shell. No overhanging lips, negative angles etc.

## Slide 8
Motion / Vehicle
Sample mould with Vacuum formed shell
Best results obtained from 2mm sheet
Other colours available

## Slide 9
Motion / Vehicle
Other possible ideas on a vehicle or motion theme:
Use of sensors: Anti crash /avoidance device
Direction change/ Light sensing
Line followers
Airport Rolling walkway
All of the processes and manufacturing techniques used in the previous example also required here.
In addition you could incorporate different drive mechanisms, load sensors, motion detectors, counters, etc.
Safety considerations

## Slide 10
Motion / Vehicle
Simple design idea for walkway
With the addition of a stairs profile and inclined at an angle you have an escalator. Add shelve plates at right angles to the belt, mount vertically and you have a dumb waiter or a simple revolving display, etc, etc.

## Slide 11
Motion / Vehicle
Summary
Some or all of the following areas may be integrated and incorporated into the final project:
Design theory and practice
Appropriate material selection
Marking out and fitting skills
Assembly and joining processes
Electronic circuit design theory and practice
Mould making theory and practice
Finishes, surface and other
Project Management
Safety considerations, general and project specific.

## Slide 12
Motion / Vehicle

## Slide 13
Motion / Vehicle
Minature electric motor
This is a small DC motor that is useful for low power projects – larger motors are available that supply more torque but require more current

## Slide 14
Motion / Vehicle
Motor connections from the rear

## Slide 15
Motion / Vehicle
Brushes – brush against the armature to bring current to the coil(s)
Motor end

## Slide 16
Motion / Vehicle
Armature: note coils of wire which carry current from brushes to create magnetism

## Slide 17
Motion / Vehicle
Magnets inside case drive armature around

## Slide 18
Motion / Vehicle
Magnets removed from case
Clip