## Slide 1: Applied Control Systems Robotics & Robotic Control

## Slide 2: Robotic Syllabus Topics
Higher & Ordinary
Robotics:
Robotic joints; degrees of freedom; coordinate frames
Forces and moments; calculations
Introduction to Robotic Control:
Classification of robots by structure; applications, with an emphasis on manufacturing applications
Principles of open and closed loop control
Principles of operation and control of d.c., servos and stepper motors.
A/D and D/A Conversion:
Analogue to digital and digital to analogue converters (A/D and D/A)

## Slide 3: Content
Introduction to Robotics
What is a robot
Degrees of freedom & Robotic joints
Classification & coordinate systems / frames
Forces and moments
Actuators, DC motors, Stepper and Servo Motors
End Effectors
Open loop
Closed loop
A/D & D/A Conversion

## Slide 4
What is a robot?
Intelligent device who’s motion can be controlled, planned, sensed. . .
Electro-mechanical system
Actions and appearance conveys it has intent of its own
Performs jobs- cheaper, faster, greater accuracy, reliability compared to human.
Widely used in manufacturing and home
Robotics

## Slide 5
Robots are machines expected to do what humans do
Robots can mimic certain parts of the human body
Human arm
Robot arms come in a variety of shapes and sizes
Size & shape critical to the robots efficient operation
Many contain elbows, shoulders which represent: - Degrees of freedom
Motors provide the ‘Muscles’
Control circuit provides the ‘Brain’
Robotics

## Slide 6
Degree of freedom - one joint one degree of freedom
Simple robots - 3 degrees of freedom in X,Y,Z axis
Modern robot arms have up to 7 degrees of freedom
XYZ, Roll, Pitch and Yaw
The human arm can be used to demonstrate the degrees
of freedom.
Crust Crawler- 5 degrees of freedom
Degrees of Freedom

## Slide 7: Robotic Joints
To provide a variety of degrees of freedom,
different robotic joints can be used: -
Rotary joints
- Waist joint
- Elbow joint
Linear/ Prismatic joints
- Sliding joints
- Simple axial direction
Sliding Link
Rotation around joint axis
Both used together to achieve required movement i.e.
‘Cylindrical Robot’

## Slide 8: Robot ‘Work Envelope’
The volume of space in which a robot can operate is called the ‘Work Envelope’.
The work envelope defines the space around a robot that is accessible to the mounting point for the end-effector

## Slide 9: Classification of Robots
Robot designs fall under different coordinate systems or frames
Depends on joint arrangement
Coordinate system types determine the position of a point through measurement (X, Y etc.) or angles
Different systems cater for different situations
The three major robotic classifications are:
        (i) Cartesian
        (ii) Cylindrical
        (iii) Spherical / Polar

## Slide 10
Most familiar system
Uses three axes at 90° to each other
Three coordinates needed to find a
point in space
The right-hand rule.
Cartesian Robot:
  Three prismatic joints
  Pick and place
Cartesian Coordinate Frame

## Slide 11
Cartesian Robot Applications
Applying adhesive to a pane of glass
Transferring ICs from a pallet to a holding location
Transferring & Stacking
Camera monitoring of products

## Slide 12: Cylindrical Coordinate Frame
Point A- located on cylinder of known radius
Height Z from origin
Third point - angle on the XY plane
Cylindrical Robot:
Used mainly for assembly
Repeatability and accuracy - Medical testing
Two prismatic joints and one rotary joint
Work Envelope

## Slide 13
Cylindrical Robot Applications
Used extensively in medical research
DNA Screening
Drug Development
Toxicology

## Slide 14: Spherical/ Polar Coordinate System
Similar to finding a point on the earth’s surface
Radius,
Latitude
Longitude
Spherical / Polar Robot:
Spot, Gas and Arc Welding
Reaching horizontal or inclined
tunnels / areas
Robot sometimes known as the gun turret
Work Envelope

## Slide 15: Polar Robotic applications
Used extensively in the car manufacturing industry
Welding

## Slide 16: The Scara Robot
Developed to meet the needs of modern assembly.
Fast movement with light payloads
Rapid placements of electronic components on PCB’s
Combination of two horizontal rotational axes and one
linear joint.

## Slide 17: Scara Robot Applications
Testing a calculator.
Camera observes
output
Stacking lightweight
components
Precision assembly
Multi Function

## Slide 18: The Revolute Robot
The Revolute or Puma most resembles the human arm
The Robot rotates much like the human waist
Ideal for spray painting and welding as it mimics human
movements
Gripper

## Slide 19: Revolute Applications
Spray Painting
Metal Inert Gas Welding

## Slide 20: The Humanoid Robot
Previously developed for recreational and
entertainment value.
Research into use for household chores,
aid for elderly aid

## Slide 21: Moments and Forces
There are many forces acting about a robot
Correct selection of servo - determined by required torque
Moments = Force x Distance
Moments = Load and robot arm
Total moment calculation
Factor of safety- 20%

## Slide 22: Actuators
Motors- control the movement of a robot.
Identified as Actuators there are three common types
  DC Motor
  Stepper Motor
  Servo motor
Stepper motor

## Slide 23: DC Motors
Most common and cheapest
Powered with two wires from source
Draws large amounts of current
Cannot be wired straight from a PIC
Does not offer accuracy or speed control

## Slide 24: Stepper Motors
Stepper has many electromagnets
Stepper controlled by sequential turning on and off of
magnets
Each pulse moves another step, providing a step angle
Example shows a step angle of 90°
Poor control with a large angle
Better step angle achieved with the toothed disc

## Slide 25: Stepper motor operation
Step1

## Slide 26
Step 2
Stepper motor operation

## Slide 27
Stepper motor operation
Step 3

## Slide 28
Stepper motor operation
Step 4

## Slide 29: Stepper Motors
3.6 degree step angle => 100 steps per revolution
25 teeth, 4 step= 1 tooth => 100 steps for 25teeth
Controlled using output Blocks on a PIC
Correct sequence essential
Reverse sequence - reverse motor

## Slide 30: Servo motors
Servo offers smoothest control
Rotate to a specific point
Offer good torque and control
Ideal for powering robot arms etc.
However:
Degree of revolution is limited
Not suitable for applications which require
continuous rotation

## Slide 31: Servo motors
Contain motor, gearbox, driver controller and potentiometer
Three wires - 0v, 5v and PIC signal
Potentiometer connected to gearbox - monitors movement
Provides feedback
If position is distorted - automatic correction
+ 5V

## Slide 32: Servo motors Operation
Pulse Width Modulation (0.75ms to 2.25ms)
Pulse Width takes servo from 0° to 150° rotation
Continuous stream every 20ms
On programming block, pulse width and output pin must be set.
Pulse width can also be expressed as a variable

## Slide 33: End Effectors
Correct name for the “Hand” that is attached to the end of robot.
Used for grasping, drilling, painting, welding, etc.
Different end effectors allow for a standard robot to
perform numerous operations.
Two different types - Grippers & Tools
End Effector

## Slide 34: End Effectors
Tools: Tools are used where a specific operation needs
to be carried out such as welding, painting drilling
etc. - the tool is attached to the mounting plate.
Grippers: mechanical, magnetic and pneumatic.
Mechanical:
Two fingered most common, also multi-fingered available
Applies force that causes enough friction between object to
allow for it to be lifted
Not suitable for some objects which may be delicate / brittle

## Slide 35: End Effectors
Magnetic:
Ferrous materials required
Electro and permanent magnets used
Pneumatic:
Suction cups from plastic or rubber
Smooth even surface required
Weight & size of object determines size and number of cups

## Slide 36: Open and Closed Loop Control
All control systems contain three elements:
(i) The control
(ii) Current Amplifiers
(iii) Servo Motors
The control is the Brain - reads instruction
Current amplifier receives orders from brain and sends
required signal to the motor
Signal sent depends on the whether Open or Closed loop
control is used.

## Slide 37: Open Loop Control
For Open Loop Control:
The controller is told where the output device needs to be
Once the controller sends the signal to motor it does not
receive feedback to known if it has reached desired position
Open loop much cheaper than closed loop but less accurate

## Slide 38: Open Loop Control

## Slide 39: Closed Loop Control
Provided feedback to the control unit telling it the actual
position of the motor.
This actual position is found using an encoder.
The actual position is compared to the desired.
Position is changed if necessary

## Slide 40: The Encoder
Encoders give the control unit information as to the actual
position of the motor.
Light shines through a slotted disc, the light sensor counts
the speed and number of breaks in the light.
Allows for the calculation of speed, direction and distance
travelled.

## Slide 41: Closed Loop Control
The desired value is compared to the actual value.
Comparator subtracts actual from desired.
The difference is the error which is fed to the controller
which generates a control action to eliminate the error.

## Slide 42: On - off control
Simplest closed loop:
When an error is identified the system goes into full
corrective state.
Can tend to over shoot desired.
Stops and falls below desired so it never reaches desired

## Slide 43: Proportional control
Rubber band effect - greater the distance from the
desired more corrective force applied.
As it approaches the desired, less correction.
Tend to reduce over shoot but slower reaction.
Never reaches desired - offset

## Slide 44: Proportional control
System attempts to calculate a Gain K that will try and stabilise the system at the desired value.

## Slide 45: AD/DA Conversion
Necessary to be able to convert analogue values to digital.
All computer systems only count using 1 &0 (Binary)
This is a counting system to the base 2
Used to the decimal system to the base 10
Digital values
Analogue values

## Slide 46: Binary Counting

## Slide 47: 8 Bit system
Logicator uses an 8 bit system.
This gives the 256 number (0 - 255)
Digital reads 0 (Off) from 0v - 0.8V
1 (On) from 2v - 5v

## Slide 48: Analogue
Analogue has a large number of values between
0v and 5v. Depends on the resolution.
Graph shows the fluctuation in voltage compared to digital.

## Slide 49: Analogue- Digital
The 5v is broken up into 256 segments.
The analogue resolution is now 256 (0 - 255).
The voltage level from the analogue input is now able to be read between 0 - 255 and not as a fluctuating voltage.
This value is now stored as a binary number in the 8 bit system
The analogue reading at an instance