## Slide 1
Applied Control Systems
Stepper Motors

## Slide 2
Stepper Motor / Electro magnet

## Slide 3
Rotor
Stator
Coils
Outside Casing
Stator
Rotor
Internal components of a Stepper Motor

## Slide 4
Stators
Rotor
Cross Section of a Stepper Motor

## Slide 5
Four Steps per revolution i.e. 90 deg. steps.
Full Step Operation

## Slide 6
Eight steps per. revolution i.e. 45 deg. steps.
Half Step Operation

## Slide 7
Winding number 1
Winding number 2
One step
6 pole rotor

## Slide 8
How many steps are required for one complete revolution?
Six pole rotor, two electro magnets.

## Slide 9
The top electromagnet (1) is turned on, attracting the nearest teeth of a gear-shaped iron rotor. With the teeth aligned to electromagnet 1, they will be slightly offset from electromagnet 2
The top electromagnet (1) is turned off, and the right electromagnet (2) is energized, pulling the nearest teeth slightly to the right. This results in a rotation of 3.6° in this example.
Practical Stepper motor operation

## Slide 10
The bottom electromagnet (3) is energized; another 3.6° rotation occurs.
The left electromagnet (4) is enabled, rotating again by 3.6°. When the top electromagnet (1) is again enabled, the teeth in the sprocket will have rotated by one tooth position; since there are 25 teeth, it will take 100 steps to make a full rotation in this example.

## Slide 11
Stepping Motor to move read-write head
Stepper motor applications

## Slide 12
Paper feeder on printers
CNC lathes
Stepper motors
Stepper motor applications

## Slide 13
Rotor
Stator coils
CNC Stepping Motor

## Slide 14
Advantages:-
Low cost for control achieved
Ruggedness
Simplicity of construction
Can operate in an open loop control system
Low maintenance
Less likely to stall or slip
Will work in any environment
Disadvantages:-
Require a dedicated control circuit
Use more current than D.C. motors
High torque output achieved at low speeds
Advantages / Disadvantages

## Slide 15
Step 1 | 0 | 0 | 1 | 1
Step 2 | 1 | 0 | 1 | 0
Step 3 | 1 | 1 | 0 | 0
Step 4 | 0 | 1 | 0 | 1
+
CW
CCW
Control sequence to turn a stepper motor

## Slide 16
Servo Motor Detail
+ 5V
Actuator
Reduction gear
Position feedback
Potentiometer
(closed loop system)
Small electric DC motor