## Slide 1
Manufacturing Systems
Rd 6 Technology
CAD/CAM

## Slide 2
Objectives
Introduce simple CNC routing techniques & principles
Experience CAD / CAM design software
Experience the use of CNC routing to: -
(i) Carry out a simple 2-D machining exercise
(ii) Manufacture a PCB
CAD/CAM Workshops

## Slide 3
Resource Material : -
Applications of CAD / CAM in Schools
Characteristics of TechSoft / Denford CNC Router
2-D Machining Exercise
PCB Manufacture Exercise
Appendix to include
Setting up the Machine & Tools
Importing a CAD Drawing in DXF format
File transfer between systems.
CAD/CAM Workshops

## Slide 4: CAD/CAM Workshops
Types of CNC machine: -
CNC Lathes - Cylinders, Tapers, Threads, Flat surfaces
Laser Technology – Accurate 2D profiles from Wood & Plastics
CNC Routers – Versatile; 2D, 3D, Scan in 3D & PCB manufacture

## Slide 5
CNC Routing
2-D profile cutting

## Slide 6
CNC Routing
PCB Manufacture
PCB Design
Machined PCB

## Slide 7: CNC Routing
3-D Machining
CAD Model
Machined Part

## Slide 8: Self Centering Vice

## Slide 9
CNC Routing
3D Scanning

## Slide 10: 2D Routing
Engraving
Raised engraving on a curved surface
Text

## Slide 11
CNC Routing
Lithopane Machining
Light Box Monochrome Images

## Slide 12
Degrees of Freedom
CNC three axis routing
Axis orientation

## Slide 13: Using a CNC Routing Machine
Main aspects: -
Working holding
Toolsetting – Datum point & Offsets
Programming – Software
Operation of the machine

## Slide 14: 2-D Machining principals

## Slide 15: Tool offsets and depths
Order / Machine Plan
Machine Pocket
Remove holes
Engrave Text
Cut through profile
2 mm Dia. Slot Cutter
1 mm contour offset

## Slide 16: TechSoft Exercise
Picture Holder

## Slide 17: TechSoft Exercise
Use setup file ‘Frame Template.CFG’
Use Template file ‘Frame TEMPLATE.dtd’
Machine part
Add Text
Edit to incorporate text in profile
Add tool path

## Slide 18: PCB Manufacture
Circuit design
PCB layout generated
Motor Control Circuit

## Slide 19: PCB Manufacture
Important Considerations
Flatness of PCB on machine table - Size
Tracks etc should be adjusted before export to CAD/CAM software
Placement of components
Track Width and Isolation Gap
Full copper removal

## Slide 20: PCB Manufacture Denford Router
Software : -
QuickCAM 2D Design - 2D profile work
VR Milling V5 - Control software, PCB manufacture
QuickCAM Pro – 3D & Lithopane Machining,

## Slide 21: PCB Manufacture Denford Router
No hazardous chemicals
Dry machine tracks using Vee engraving tool
Drill holes using PCB drill
Or
Spot with vee tool and drill by hand

## Slide 22: Specific Neutral File formats
Gerber Files
Required by VR Milling for PCB production
Created as a set – one layer to a file
Need to identify which file contains items of interest
Drill file
Solder Side

## Slide 23: TechSoft Exercise
Software: -
TechSoft 2D Design - 2D Machining
Techsoft PCB Design & Make – PCB manufacture
Visual Tool Path - 3D machining