## Slide 2: First construct the given elevation, be sure to label points A,B,C which oblique plane cuts through

## Slide 3: Send down all key points in construction to set up the plan

## Slide 4: Draw in a plan as given in the question, again mark in A,B,C as these are key points of the question

## Slide 5: Join points A,B,C in both elevation and plan to create a common triangular plane

## Slide 6: Treat the triangular plane as you would a triangle in a planes question and find a true line coming from B by drawing a horizontal line from B in the elevation and then find it in the plan

## Slide 7: Draw the construction looking in, in the direction of the arrow and set up a X1,Y1 line perpendicular to the projected lines

## Slide 8: As always for a auxiliary take critical heights from two views back to mark off in this case H1,H2 and H3. X1,Y1 is the ground line

## Slide 9: Draw in the auxiliary view and show all hidden detail

## Slide 10: Draw the cutting plane through points A2,B2 and C2

## Slide 11: All the points which the cutting plane pass through project back up to the plan

## Slide 12: Where the lines from the auxiliary touch the plan project these up to the elevation

## Slide 13: The red lined area is the section which is cut by the plane this is set up by joining all the projected lines from the auxiliary up

## Slide 14: You can now heavy in the final shape as shown below

## Slide 15: Finally draw in sectioning into the cut area, question is now complete