## Slide 1: L.C. Technology
Professional Development for Teachers

## Slide 2: Feedback
  Very positive response to Line following Robot.
  Genie E18 motor board used to control robot, 2 LDR’s were used to provide feedback to control position of robot

## Slide 3: J’Cert Technology Projects
Junior Certificate Projects covered
Mobile Phone Holder
Desk Tidy
DVD Rack
Mood Light
Desktop Light
Photo Display
Bird House

## Slide 4
Leaving Certificate
Technology
Sample Robotics Project

## Slide 5: Design Task
Design and make a 3 Axis Pick and Place Robot which is capable of moving a small load from one position to another.

## Slide 6: Syllabus Topics Addressed

## Slide 7: Suggested Methodology
There are a number of approaches to this project.
Option 1:
Basic control of servo motors using control software to programme a 3 axis robot arm. The arm is to move to various locations and provide pick and place capabilities.
Option 2:
Design a separate control panel to provide:
(i) control of two axis using 2 potentiometers.
(ii) a means of operating a gripper using an LDR
Option 3:
Challenge students to design a robotic system which will separate different coloured balls / blocks into various containers.

## Slide 8: Focus for this Round.
Option 1 & 2:-
3- axis Robotic arm controlled by Genie E18 Motor Board
3 Servo motor outputs

## Slide 9
Materials Required
E18 Genie Motor Board populated for servo motor control
3 Servo-Motors and attachments
Acrylic sheet 1000 x 500 x 5 mm/3mm
5 of 35mm x 8 dia. plastic tube, threaded M5 one end
5 of M5 x 20mm cheese head screws
4 of M4 x 20 cheese head screws and 8 nuts
4 of M4 x 12 cheese head screws and nuts
1 of M3 x 20mm cheese head screws and 2 nuts
1 of M2.5 x 12mm cheese screw with locknut
280mm of diameter 1.5 mm mild steel rod
3 servo motor extension leads

## Slide 10: Health & Safety
The technology room Health and safety rules and regulations apply.
Hazards specific to this project include the following:
  Drilling acrylic and the risk of cracking.
  Potential bonding of body tissue due to the use of adhesives. The attention of students should be drawn to this hazard and proper precautions should be taken to minimise this risk.
  Possible cutting from metal swarf on the end of mild steel rod. Students attention should be drawn to this hazard and the mitigation of the risk by removing the swarf with a file after cutting.

## Slide 11: End Effectors for Robot
Mechanical Grippers
Magnetic Grippers
Vacuum Grippers
Electro-Magnetic Gripper

## Slide 12: Sample Calculation
If the weight of the servo motor equals 0.324N, calculate the mass of A, which will allow the robotic arm rotate a mass of 180g to a new position without the risk of toppling over.
A
24cm
105mm

## Slide 13: Answer
Clockwise moment = Anti-clockwise moment
1.77N x .24 m = (0.324N x .07m) + (Force x .105m)
.42Nm = 0.022Nm + (Force x .105m)
.42Nm– 0.022Nm = .105m x Force
.398Nm = .105m x Force
.398/.105 = Force
3.79N = Force
Mass of A = 3.79 / 9.81
.386kg = 386 g
180Kg x 9.81 = 1.77N
24cm
105mm
A

## Slide 14: Assessment
Students could be asked to carry out research on a theme based on automation in the workspace / home / leisure / other?
Students could be asked to consider how the product could best be manufactured and to compile a Gantt chart which displays the manufacturing sequence for the project.

## Slide 15: Assessment
The functionality, quality and finish of the product could be assessed by the class teacher using assessment guidelines given by State exams
Artefact meets theme
Originality and Creativity
Production Skills
Functionality
Quality and Finish
Presentation of Artefact

## Slide 16
THE END