## Slide 1: L.C. Technology Servo Motor Control / Genie Software
Professional Development for Teachers

## Slide 2
Introduction to the Servo
Servo offers smoothest control
Rotate to a specific point
Offer good torque and control
Ideal for powering robot arms etc.
However:
Degree of revolution is limited
Not suitable for applications which require
continuous rotation

## Slide 3: Servo Motors
Contain motor, gearbox, driver controller and potentiometer
Three wires - 0v, 5v and PIC signal
Potentiometer connected to gearbox - monitors movement
Provides feedback
If position is distorted - automatic correction

## Slide 4: Servo Motor Operation
Servo Motor selected from list
On programming block, pulse width and output pin must be set.
Option for speed control in seconds
Pulse width can also be expressed as a variable

## Slide 5: Pulse Width
Pulse Width Modulation (0.75ms to 2.25ms)
Pulse Width takes servo from 0° to 150° rotation
Continuous stream every 20ms

## Slide 6: Genie E18 Motorboard
Servo Outputs
Motor board offers three servo outputs
Outputs must be linked directly to PIC and not from transistor chip
Designated outputs – Q0, Q1, Q2

## Slide 7: Genie E18 Motorboard
Analogue Inputs
Inputs that have varying resistance
Three designated analogue inputs- A0, A1, A2
Genie uses the variance and assigns values from 0-255